LimiFrog PCB Assembly Test Program
Documentation
(v0.4)

An overview of LimiFrog's physical interfaces (connectors, switches and indicators) is provided at the end of this document.

Program LimiFrog_PCBA-Test exercizes various functionalities of the LimiFrog board.
It is intended to test the LimiFrog board after PCB assembly.

Code Dowload

The code is provided as .bin (pure binary code), as produced by the GNU compiler and linker for ARM. It must be loaded into Flash at address 0x08000000.
Code may be downloaded through the STM32 SWD serial interface of LimiFrog.
This interface features a clock pin SWCK and a data pin SWDIO. No reset pin is implemented.
Power can be supplied to the board either through the VCC pin (3-3.3V range), through the battery connector (3.6-4.2V range) or through the USB connector (5V nominal). In the latter 2 cases, VCC will be generated by the on-board PMIC and the voltage measured on the VCC pin should be 2.93V +-5%.

Pass / Fail Criteria

The code is mostly self-checking. Additional probing of the extension port, as described below, provides additional coverage.

The general purpose Red LED D4 emits a brief flash upon start of the test program.
Then, upon completing, the program returns the following status :
> FIXED red LED D4	= PASS
> FLASHING red LED	= FAIL
> LED stays OFF	= FAIL, program has not terminated

In addition, probing the extension port after test program execution should yield the following results (naming conventions indicated in the figure below) :
- Position 1: Logic_1 (VCC)
- Position 2: Logic_1 (VCC)
- Position 3: Logic_1 (VCC)
- Position 4: Logic_1 (VCC)
- Position 5: VCC_LDO, 3.3V nominal
- Position 6: Logic_1 (VCC)
- Position 7: Logic_1 (VCC)
- Position 8: GND
- Position 9: Logic_1 (VCC)
- Position 10: Logic_1 (VCC)